## Slide 1: Biomedical Image Enhancement using Hybrid Techniques
Presented by:
Anem GnanaGanesh
Chinthamani Manoj Ram Sai
Annam Yogitha
Contact:
backpropbrigade@gmail.com

## Slide 2: Contents
Introduction
Problem Statement
FBP Metrics
Preprocessing in Sinogram Domain
Post Processing in Image Domain
TV Regularization Method
Learned Primal Dual Method
Progress
Timeline

## Slide 3: Problem statement
Noisy CT
Clean CT
Noisy MRI
Clean MRI
Why Image Enhancement is critical?
Why Hybrid Techniques?

## Slide 4: LoDoPaB - CT : Benchmark dataset for Low Dose reconstruction
&
n
Designed for evaluating reconstruction methods in low-dose settings.
Provides a standard benchmark for comparing deep learning classical methods.
~40,000 slices from 812 patients (LIDC/IDRI database).
Simulated low-dose parallel-beam CT.
Corrupted with Poisson noise → mimics real low-photo measurements.
Resolution: 362 × 362 px cropped thoracic CT slices.
Projections: 1000 angles × 513 detector pixels per slice.
Lodopab-CT
┌─────────┴────────┐
Observation (Sinogram)
┌────┼────┐
Ground Truth
┌────┼────┐ Train Validation Test
Train Validation Test
X-axis: Detector index (pixels)
Y-axis: Projection angles (degrees)
Characteristics:

## Slide 5: Mean metrics for test set (different filters) - FBP reconstruction
Filter(Frequency scaling) | PSNR | SSIM
Hann_0.641 | 30.516 + 3.097 | 0.7372 + 0.1467
Hann_0.8 | 30.445 + 3.373 | 0.7088 + 0.1563
Hann_1.0 | 29.799 + 3.629 | 0.6626 + 0.1685
Hamming_1.0 | 29.507 + 3.681 | 0.6464 + 0.1714
Cosine_1.0 | 28.387 + 3.879 | 0.5904 + 1800
SheppLogan_1.0 | 25.494 + 4.078 | 0.4654 + 0.1782
RamLak_1.0 | 23.880 + 4.140 | 0.4029 + 0.1688

## Slide 6: Comparison of Metrics

## Slide 7: Best Mean Metrics for FBP(Hann_0.641)
Set | PSNR | SSIM
Train | 30.452 + 2.654 | 0.7415 + 0.1314
Validation | 30.752 + 2.518 | 0.7577 + 0.1231
Test | 30.516 + 3.097 | 0.7372 + 0.1467
6

## Slide 8: Preprocessing with Different Filters in Sinogram Domain (Test Set Mean Metrics)
Filter | PSNR (db) | SSIM | PSNR(loss/gain) | SSIM(loss/gain) | Best Parameters
Median | 30.371 | 0.742 | -0.145 | 0.004 | kernel Size: 3
Bilateral | 30.237 | 0.745 | -0.279 | 0.007 | d: 3 sigma_color: 0.01 sigma_spatial: 10.0
Gaussian | 30.516 | 0.737 | 0 | -0.0002 | sigma: 0.1 truncate: 3.417201 filter Size: 1
Wavelet denoising | 30.527 | 0.74 | 0.011 | 0.0028 | sigma_scale: 1.1795 wavelet: bior1.3 mode: soft
TV denoising | 29.966 | 0.736 | -0.55 | -0.0012 | TV weight: 0.0010
Non Local Means | 30.516 | 0.737 | 0 | -0.0002 | h (filter strength): 0.0741 patch size: 3 Search window: 21

## Slide 9: Post Processing with Different Filters in Image Domain (Test Set Mean Metrics)
Filter | PSNR (db) | SSIM | PSNR(loss/gain) | SSIM(loss/gain) | Best Parameters
Median | 30.702 | 0.753 | 0.186 | 0.0158 | kernel Size: 5
Bilateral | 31.007 | 0.755 | 0.491 | 0.0178 | d: 9 sigma_color : 0.03329 sigma_spatial: 10.0
Gaussian | 30.504 | 0.742 | -0.0012 | 0.0048 | sigma: 0.563682 truncate: 4.522496 filter Size: 7
Wavelet denoising | 30.543 | 0.739 | 0.027 | 0.0018 | sigma_scale: 3.0 wavelet: coif1 mode: soft
TV denoising | 30.761 | 0.758 | 0.245 | 0.0208 | TV weight: 0.0113
Non Local Means | 30.516 | 0.737 | 0 | -0.0002 | h (filter strength): 0.5 patch size: 3 Search window: 21

## Slide 10: Why CT Reconstruction is an Inverse Problem
Equations & Explanation: Why direct inversion fails:
y=Ax+ε
x → unknown image (slice of body)
A → forward operator (Radon transform)
y → measured projections (sinogram)
ε→ noise (Poisson)
Forward Operator (Radon Transform):
(Ax)(θ, t) = ∫_L(θ,t) x(s) ds
Integrates image values along each X-ray line
Each measurement = total attenuation along that path
Collect all lines → sinogram
CT reconstruction is an inverse problem. Noise and incomplete projections make direct inversion unstable, motivating regularized iterative methods.
FBP: direct inversion → noisy, streak artifacts
Ill-posed because:
Noise amplified (ε≠0)
Limited angles / incomplete data
Goal: Recover x reliably → need regularization

## Slide 11: Total Variation (TV) Regularization
Core Idea
Reconstruct the CT image by minimizing a balance between data-fidelity and total variation (gradient sparsity) to promote piecewise-smooth images.
Algorithm Flow
Initialize image x0 = FBP(y)
Iterate:
Forward projection: Ax_k
Compute loss: L(x_k) Compute gradient: ∇L(x_k) =
Update x_(k+1) using Adam optimizer
Track best reconstruction
Output: x* = best reconstruction
+
Loss Function :
10

## Slide 12: TV Reconstruction

## Slide 13: TV Reconstruction

## Slide 14
500 Iterations
1000 Iterations

## Slide 15: Mean Metrics for TV Reconstruction
For 1000 iterations | PSNR (db) | SSIM | MSE | MAE
Validation | 32.24 | 0.824 | 0.0002 | 0.0089
Test | 31.42 | 0.781 | 0.0003 | 0.0107
14

## Slide 16: Learned Primal - Dual Reconstruction
Core idea:
Learn an iterative algorithm that alternates primal (image) and dual (data) updates.
Each update step is replaced by a learned CNN block, while still using the CT forward model and its adjoint.
Algorithm
Initialize primal image and dual .
For each iteration k = 1,…,K :
  Dual Update:
  Primal Update:
Output final reconstructed image .

## Slide 17: Learned Primal - Dual Reconstruction

## Slide 18: Learned Primal - Dual Reconstruction

## Slide 19: Mean Metrics for Learned Primal Dual Reconstruction
 | PSNR | SSIM | MSE | MAE
Validation | 36.9281 | 0.8844 | 0.0001 | 0.0069
Test | 36.0520 | 0.85 | 0.0002 | 0.0086
18

## Slide 20: Analysis - Test Set Results
Method | PSNR | SSIM | PSNR | SSIM
FBP | 30.516 | 0.7372 | 30.45 | 0.7415
TV | 31.42 | 0.781 | 33.36 | 0.830
Learned PD | 36.052 | 0.85 | 36.25 | 0.866
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=10979336
Proposed FAST-DDPM diffusion model reconstructs full-dose CT from 10% low-dose input, achieving
37.5 dB PSNR and 0.92 SSIM on the evaluation set (38 train + 10 test patients).
https://www.nature.com/articles/s41597-021-00893-z https://www.mdpi.com/2313-433X/7/3/44
Challenge Set

## Slide 21: Progress
Completed :
Applied FBP on LoDoPaB-CT dataset.
Explored multiple filters: Hann, Hamming, Cosine, RamLak, Shepp Logan.
Preprocessing and Post Processing: Bilateral, Gaussian, Wavelet, Median, TV denoising, Non Local Means, Anscombe transform
Deep Learning Enhancement - Trained U-Net on enhanced images obtained from FBP.
Applied TV Regularization on LoDoPaB-CT dataset.
Applied Learned PD on LoDoPaB-CT dataset.
Future Work :
  Extend experiments to other CT datasets: SynthRAD, AAPM Low-Dose Challenge, or Mayo Clinic datasets.
  Cross-scanner and cross-dose generalization.
  Exploring deep learning reconstruction networks.
  Assess impact on downstream tasks such as segmentation or lesion detection.
20

## Slide 22: Timeline
Phase 2
P
Exploring FBP + Mathematical filters + Pre and Post processing methods
Phase 1
Literature Review (Research papers)
Phase 6
Assessing downstream task performance to quantify clinical relevance of the enhancement
Phase 3
Exploring Total Variation Regularization and Learned Primal Dual methods.
Phase 4
Combining classical methods with deep learning for enhancement
Phase 5
21
Extensive and rigorous testing on multi-site, multi-acquisition datasets to quantify the generalizability

## Slide 23: THANK YOU
22